## Slide 1: Predicting the energy output of wind turbine based on weather condition
TEAM MEMBERS
NAGUL V
RAHUL ASWIN R
SANTHOSH RAJ K
SRIRAM J

## Slide 2
LITERATURE
SURVEY

## Slide 3: Forecast of Regional Power Output of Wind Turbines
Authors : Hans Georg Beyer , Detlev Heinemann, Harald Mellinghoff, Kai M¨onnich, Hans-Peter Waldl
A method for predicting the power output of wind turbines connected to the public electricity grid will be introduced. Using this procedure it is possible to forecast – over a time horizon of 6 - 48 hours – the wind power to be expected. Base of the method are the operational, large scale wind field predictions of the numerical Deutschlandmodell of the german weather service DWD. For wind power forecast, these predictions have to be spatially refined. The local roughness and orography conditions have to be taken into consideration for this. The procedure has been used for wind and power prediction for several sites distributed over the northern part of Germany. The quality of the predictions will be discussed in comparison to measured values of a one-year database.

## Slide 4: Using machine learning to predict wind turbine power output
Authors : A Clifton, L Kilcher, J K Lundquist and P Fleming
Wind turbine power output is known to be a strong function of wind speed, but is also affected by turbulence and shear. In this work, new aerostructural simulations of a generic 1.5 MW turbine are used to rank atmospheric influences on power output. Most significant is the hub height wind speed, followed by hub height turbulence intensity and then wind speed shear across the rotor disk. These simulation data are used to train regression trees that predict the turbine response for any combination of wind speed, turbulence intensity, and wind shear that might be expected at a turbine site. For a randomly selected atmospheric condition, the accuracy of the regression tree power predictions is three times higher than that from the traditional power curve methodology. The regression tree method can also be applied to turbine test data and used to predict turbine performance at a new site. Such an approach could significantly reduce bias in power predictions that arise because of the different turbulence and shear at the new site, compared to the test site.

## Slide 5: Short-term prediction of the power production from wind farms
Author : L. Landberg
This paper describes a model for prediction of the power produced by wind farms connected to the electrical grid. The time frame is from 0 to 36 h ahead. The goal is to develop a model that can be integrated in the dispatching system at a utility. The physical basis of the model is the predictions generated from forecasts from the high-resolution limited area model (HIRLAM) of the Danish Meteorological Institute. These predictions are then made specific for individual sites (wind farms) by applying a matrix generated by the submodels of WASP (Wind Atlas Application and Analysis Program). To verify the model one year's worth of data from 17 wind farms have been used. The farms are located in Denmark on the Zealand (14) and Bornholm (3) islands and are all controlled by the Danish utility ELKRAFT/SK Power.

## Slide 6: Predicting the Energy Output of Wind Turbine Based on Weather Condition
Authors : P. R. Anisha, C. Kishor Kumar Reddy, Nuzhat Yasmeen
Wind energy plays an increasing role in the supply of energy worldwide. The energy output of a wind farm is highly dependent on the weather conditions present at its site. If the output can be predicted more accurately, energy suppliers can coordinate the collaborative production of different energy sources more efficiently to avoid costly overproduction. In this paper, we take a computer science perspective on energy prediction based on weather data and analyze the important parameters as well as their correlation on the energy output. To deal with the interaction of the different parameters, we use random forest regression of machine learning algorithms. Our studies are carried out on publicly available weather and energy data for a wind farm. We report on the correlation of the different variables for the energy output. The model obtained for energy prediction gives a very reliable prediction of the energy output for supplied weather data.

## Slide 7: Predicting the energy output of wind farms based on weather data
Authors: Ekaterina Vladislavleva, Tobias Friedrich, Frank Neumann, Markus Wagner
Wind energy plays an increasing role in the supply of energy world wide. The energy output of a wind farm is highly dependent on the weather conditions present at its site. If the output can be predicted more accurately, energy suppliers can coordinate the collaborative production of different energy sources more efficiently to avoid costly overproduction. In this paper, we take a computer science perspective on energy prediction based on weather data and analyze the important parameters as well as their correlation on the energy output. To deal with the interaction of the different parameters, we use symbolic regression based on the genetic programming tool DataModeler. Our studies are carried out on publicly available weather and energy data for a wind farm in Australia. We report on the correlation of the different variables for the energy output. The model obtained for energy prediction gives a very reliable prediction of the energy output for newly supplied weather data.

## Slide 8: Short-Term Prediction of Wind Farm Power : A Data Mining Approach
Authors : Andrew Kusiak, Haiyang Zheng, Zhe Song
This paper examines time series models for predicting the power of a wind farm at different time scales, i.e., 10-min and hour-long intervals. The time series models are built with data mining algorithms. Five different data mining algorithms have been tested on various wind farm datasets. Two of the five algorithms performed particularly well. The support vector machine regression algorithm provides accurate predictions of wind power and wind speed at 10-min intervals up to 1 h into the future, while the multilayer perceptron algorithm is accurate in predicting power over hour-long intervals up to 4 h ahead. Wind speed can be predicted fairly accurately based on its historical values; however, the power cannot be accurately determined given a power curve model and the predicted wind speed. Test computational results of all time series models and data mining algorithms are discussed. The tests were performed on data generated at a wind farm of 100 turbines. Suggestions for future research are provided.

## Slide 9: Virtual Models for Prediction of Wind Turbine Parameters
Authors : Andrew Kusiak and Wenyan Li
In this paper, a data-driven methodology for the development of virtual models of a wind turbine is presented. To demonstrate the proposed methodology, two parameters of the wind turbine have been selected for modeling, namely, power output and rotor speed. A virtual model for each of the two parameters is developed and tested with data collected at a wind farm. Both models consider controllable and noncontrollable parameters of the wind turbine, as well as the delay effect of wind speed and other parameters. To mitigate data bias of each virtual model and ensure its robustness, a training set is assembled from ten randomly selected turbines. The performance of a virtual model is largely determined by the input parameters selected and the data mining algorithms used to extract the model. Several data mining algorithms for parameter selection and model extraction are analyzed. The research presented in the paper is illustrated with computational results

## Slide 10: Development of small domestic wind turbine with scoop and prediction of its annual power output
Authors : F.Wang, L.Bai, J.Fletcher, J.Whiteford, D.Cullen
Based on an unperturbed airflow assumption and using a set of validated modelling methods, a series of activities were carried out to optimise an aerodynamic design of a small wind turbine for a built up area, where wind is significantly weaker and more turbulent than those open sites preferable for wind farms. These activities includes design of the blades using a FORTRAN code; design of the nose cones and nacelles, which then constituted the rotor along with the blades; optimisation of the rotor designs in the virtual wind tunnel developed in the first part of the study; and finally, estimation of the annual power output of this wind turbine calculated using hourly wind data of a real Scottish Weather Station. The predicted annual output of the finalised rotor was then compared with other commercial turbines and result was rather competitive.

## Slide 11: Analysis of wind power generation and prediction using ANN: A case study
Authors : M. Carolin Mabel, E. Fernandez
Many developing nations, such as India have embarked upon wind energy programs for areas experiencing high average wind speeds throughout the year. One of the states in India that is actively pursuing wind power generation programs is Tamil Nadu. Within this state, Muppandal area is one of the identified regions where wind farm concentration is high. Wind energy engineers are interested in studies that aim at assessing the output of wind farms, for which, artificial intelligence techniques can be usefully adapted. The present paper attempts to apply this concept for assessment of the wind energy output of wind farms in Muppandal, Tamil Nadu (India). Field data are collected from seven wind farms at this site over a period of 3 years from April 2002 to March 2005 and used for the analysis and prediction of power generation from wind farms. The model has been developed with the help of neural network methodology. It involves three input variables—wind speed, relative humidity and generation hours and one output variable-energy output of wind farms. The modeling is done using MATLAB toolbox. The model accuracy is evaluated by comparing the simulated results with the actual measured values at the wind farms and is found to be in good agreement.

## Slide 12
THANK YOU